## Slide 1
GEOLOGY OF KEMPFIELD SILVER-BARITE AND BASE METAL (Pb-Zn) VOLCANOGENIC MASSIVE SULPHIDE DEPOSIT (VMS), LACHLAN OROGEN, EASTERN AUSTRALIA
Vladimir David
Argent Minerals Ltd
McCarron Zone
BJ Zone
Quarries Zone
“The Lodge”
Argent field office

## Slide 2
History of mining
Gold in Trunkey region (Abercrombie River) was found 1851 by E Hardgrave;
Gold mining started soon after and town of Trunkey was established 1869 under name Arthur (after Joe Arthur), mining lasted for several decades;
Town change name to Trunkey in 1988 inspired by a prospector with a particularly large nose;
Imperial Herald, 1898

## Slide 3
McIntyre Mines (Australia) Pty Ltd (1970-1971);
International Nickel Australia Ltd (1972 – 1975);
The Shell Company of Australia Ltd (1979 – 1983);
Jones Mining Ltd (1984 – 1985);
Golden Cross Resources (1988 – 2004); and
Argent Minerals Limited (2007 – recent).
History of exploration
Mineral Potential Prospectivity and Risk Analysis Workshop – Black Stamp Pub venue
Imperial Herald, 1898

## Slide 4
THOMSON OROGEN
NEW ENGLAND
OROGEN
SYDNEY – BOWEN
BASIN
CURNAMONA
PROVINCE
LACHLAN OROGEN
WESTERN AND SOUTHWESTERN BELT
CENTRAL BELT
TMI image
EASTERN BELT
Kempfield
Geological setting
HET

## Slide 5
VMS deposits in
Hill End Trough
Deposit
Kempfield
Lewis Ponds
Sunny Corner
Commonwealth
21Mt @ 47g/t Ag, 0.12g/t Au and 1.92% Pb+Zn
6.35Mt @ 1.5g/t Au, 0.2% Cu, 68g/t Ag and 3.6% Pb+Zn
1.5Mt @ 0.3 g/t Au, 0.4% Cu, 24g/t Ag and 5.8% Pb+Zn
0.1Mt @ 6 g/t Au, 0.5% Cu; 250g/t Ag and 13% Pb+Zn
Resources
Bouger gravity
Hill End Trough

## Slide 6
Exploration work
Geophysics
Ground magnetics;
Gravity;
Ground EM (E-37 and SIROTEM)
Airborne magnetics – heliomag;
IP survey dipole-dipole survey;
IP survey – pole-dipole survey;
VTEM survey; and
DH electromagnetics and IP.
Geology
Structural-geological mapping and petrographic studies.
Geochemistry
Conventional soil sampling.
Drilling
491 holes (41,568m including 70 diamond holes 7,551m)
Quarries
Mather Zone
McCarron Zone
South
Conglomerate
BJ Zone
Hill Zone
Causeway

## Slide 7
Kempfield Geology Column
ORDOVICAN BASEMENT
HILL END TROUGH
unconformity
Kangaloolah Volcanics
volcanoclastic, re-worked volcanics and sediment (in upper part minor allochthonous crinoidal limestone/dolomite;
host rock for Ag-barite and Zn/Pb mineralisation
- sediments -unaltered barren siltstone with tuffaceous beds – hangingwall lithology
- felsic volcanics , rhyolithe porphyry and tuffaceous rocks – footwall sequence
- tremolite schists, biotite hornfels, a porphyritic andesite and black carbonaceous slate intruded with Silurian granites
Silurian
granite
Graphic log
Lithology description
Sequence

## Slide 8
Kempfield Geology - drillcore
- volcanic breccia and re-worked volcanoclastics (sericite alteration with carbonate and barite veins, locally silicified);
mineralised unit; BJ Zone
- fine-grained sediments with minor felsic tuffs with crenulation cleavage; hangingwall sequence; (BJ Zone)
Kangaloolah Volcanics
- banded barite with disseminated pyrite in intense sericite altered volcanoclastics

## Slide 9
Kempfield Geology – barite lenses
Outcropping massive barite lens in volcanic units of Kangaloolah Volcanics (west of Kempfield deposit)

## Slide 10
Kempfield Geology – outcropping volcanic unit
Sericite altered rhyolite; rhyolite agglomerate , locally silicified with quartz veins and disseminated pyrite
Outcropping rhyolite breccia in volcanic units of Kangaloolah Volcanics (Causeway)

## Slide 11
W
E
Copperhannia Thrust
Quarries
Mather Zone
McCarron Zone
South
Conglomerate
BJ Zone
Geology Map
Hill Zone
Causeway
Structural pattern:
NE trending Copperhannia Thrust with associated steeply dipping antithetic faults;
NW trending faults are interpreted to be vertical with dip-slip and left-lateral sense of movement developed to accommodate differential displacement Copperhannia Thrust.
McCarron Zone
BJ Zone
Copperhannia Trrust
500m
HILL END TROUGH
MUMBIL
SHELF
ORDOVICAN
BASEMENT
ORDOVICAN
BASEMENT
Geological relation:
- Basin sequence increases thickness to east;
- Basin sequence increases thickens to the northeast (basin long axis is plunging 20 º to NE).
W
E

## Slide 12
Quarries
Mather Zone
McCarron Zone
South
Conglomerate
BJ Zone
Kempfield Gravity
- Bouger gravity terrain corrected;
Bouger correction density 2.67 T/m3
- Gravity survey at 50m spacing on 100m apart lines;
- Survey conducted in two stages by Shell (1983) and Argent (2013);
- Identifies accumulation of barite masses associated with sulphides have gravity response;
- Response to basement architecture and mafic volcanics;
500m
LEGEND
Mineralisation outlines;
> 10g/t Ag in fresh rocks
Major Faults
Hill Zone
Geophysical signature

## Slide 13
Quarries
Mather Zone
McCarron Zone
South
Conglomerate
BJ Zone
Hill Zone
Causeway
Collected 3000 samples at 25m spacing on 100m apart lines by Shell, Golden Cross and Argent Mineral
Conventional soil sampling had been used to identify outcropping and sub cropping mineralisation including alteration halo
Conventional soil
Ag
500m
Ag content is soil correlates very well with subcropping mineralisation.
LEGEND
Mineralisation outlines;
> 10g/t Ag in fresh rocks
Major Faults
Geochemical signature

## Slide 14
Mather Zone
McCarron Zone
South
Conglomerate
BJ Zone
Quarries
Hill Zone
Causeway
correlates well with sub-cropping mineralisation at Quarry Zone and McCarron South;
cause false alarm at South Conglomerate and Hill Zone;
no response at BJ zone (cover of alluvial gravel)
500m
LEGEND
Mineralisation outlines;
> 10g/t Ag in fresh rocks
Major Faults
Mineralisation outlines;
> 0.5 % Pb in fresh rocks
Conventional soil
Pb
Geochemical signature

## Slide 15
Kempfield deposit geometry
Three main and several small mineralised zones :
Main zones:
- BJ Zone - barite-silver rich zone;
McCarron Zone - disseminated Ag- Pb-Zn and barite locally massive Pb-Zn sulphide (Pb-Zn);
Quarries Zone (northern) – zone of high barite and silver.
Remaining zones:
South Conglomerate Zone (low grade Ag-barite);
Mather Zone (Pb-Zn mineralisation);
Hill Zone (high grade barite and low grade Ag);
Causeway Zone (low grade Au- mineralisation hosted in a sericite altered rhyolite).
Quarries
Mather Zone
McCarron Zone
South
Conglomerate
BJ Zone
Hill Zone
Causeway
500m
Copperhannia Thrust
Mineralisation outlines;
> 10g/t Ag in fresh rocks
Mineralisation outlines;
> 0.1 g/t Au in fresh rocks
Mineralisation outlines;
> 0.5% Zn in fresh rocks
Mineralisation outlines;
> 0.5% Pb in fresh rocks
LEGEND
W
E

## Slide 16
Kempfield Geology – Cross section
volcanoclastics
volcanics
sediments
sediments
base of weathering
McCarron Zone
BJ Zone
increasing
Pb-Zn content with depth
increasing
Pb-Zn content with depth
mineralisation
mineralisation
50m
750 m
700 m
750 m
700 m
650 m
Interpretation by Argent Minerals Ltd., 2013
W
E

## Slide 17
Kempfield – Cross section geochemistry
McCarron Zone
McCarron Zone
McCarron Zone
BJ Zone
BJ Zone
BJ Zone
Base of oxidation
surface
700 mRL
700 mRL
650 mRL
Ag distribution
Pb distribution
Zn distribution
Base of oxidation
surface
700 mRL
700 mRL
650 mRL
Base of oxidation
surface
700 mRL
700 mRL
650 mRL
LEGEND
> 50 g/t Ag
< 10 g/t Ag
LEGEND
> 1% Zn
< 0.1% Zn
LEGEND
> 1% Pb
< 0.05% Pb
- a trend of increasing base metals grades (Pb-Zn) is observed laterally from the BJ Zone (predominantly Ag-barite) in the east to the McCarron Zone in the west
- barite and Ag grade are decreasing with depth, whilst Pb, Zn, Au are increasing in each individual ore system
E
E
E
W
W
W

## Slide 18
Kempfield alteration and mineralisation
Alteration assemblage at Kempfield deposit is dominated with pervasive barite, sericite/muscovite, chlorite and disseminated quartz, sulphides and a minor albite.
Mineralisation: oxide (Ag-barite) mineralisation and primary (sulphide)
Oxide mineralisation: goethite and jarosite associated with chlorargyrite, native silver and argentite in a barite gauge.
Primary (sulphide) mineralisation: pyrite is the main sulphide mineral, with Fe-poor sphalerite, argentite, native silver and Ag-sulphosalts (tetrahedrite, proustite-pyrargyrite), galena (containing pearceite-polybasite) and minor chalcopyrite.
Base of oxidation (30m - 70m)

## Slide 19
Oxide
Mineralisation
Kempfield Mineralisation
Slabbed drill core -weakly foliated, gossanous, goethite-impregnated talc-quartz rock. The pale grey aggregates are quartz and the darker brown zones contain considerable sulphide boxwork structures.
Composite aggregate of argentite-acanthite (pale grey), Pb oxidate phase (brownish-grey) and tiny creamy grains of silver-electrum, in goethite-impregnated talc.
Relict boxworks after pyrite grains, hosted in clay-degraded, goethite-impregnated talc.
view 1 mm across
View2.5 mm across
Curtsey of P. Ashley
Curtsey of P. Ashley

## Slide 20
Kempfield Mineralisation
Foliated barite-rich rock (slabbed drill core) with disseminated suplhides (sphalerite and pyrite).
Sulphide mineralisation - aggregate of argentite-acanthite (pale greenish-grey), galena (silvery grey) and sphalerite (mid grey) in a barite-rich matrix (dark grey).
Sulphide mineralisation - sphalerite (pale grey) and pyrite (pale creamy) grains in barite (darker grey). Galena (silvery) and a small grain of pale olive-grey tetrahedrite are associated with sphalerite.
Sulphide
Mineralisation
View2.5 mm across
View2.5 mm across
Curtsey of P. Ashley
Curtsey of P. Ashley

## Slide 21
Model 2
Deposit is an outcropping distal part (Ag-barite) of a larger VMS system where the base metal rich feeder zone is buried at depth or eroded.
Kempfield – deposit model
According to the structural geological relations and metal/alteration zonation, two possible genetic models can be applied:
Model 1
Deposit is a part of the spectrum of VMS deposits - a strabound barite-rich mineralisation with low grade zinc-lead-silver and it is at the low temperature end of the sea floor VMS spectrum defined by Large et al, (2001).
The apparent repetitions of mineralised barite horizons may be due to deformation and/or the presence of multiple mineralised layers within the original sequence.

## Slide 22
Kempfield ore deposit – Model 1
After Large et al, 2001
Sunny Corner,
Lewis Ponds,
Commonwealth
McPhillamy ??
Kempfield

## Slide 23
Kempfield ore deposit – Model 2
Ordovician
metasediments
Silurian
granite
Sericite - chlorite –pyrite
Massive sulphides
Zn – Pb – Ag – Ag - Cu
Sulphide stringers
Zn – Pb - Ag
Massive barite and diss. Py + Ag
Interpreted and restored precursor stratabound Kempfield deposit.
The deposit is deformed and distorted by antithetic normal faults developed at the hinterland of Copperhania Thrust as a result of extensional stress distribution and anticlockwise block rotation. The block rotation forms the apparent repetitions of mineralised lenses.
chlorite-sericte –pyrite
sediments
volcanics
McCaron Zone
BJ Zone

## Slide 24
Diagram showing possible settings of VMS deposits in convergent margins (Huston et al 2010)
Kempfield ore deposit model
Kempfield ?

## Slide 25
Disclaimer
This material contains certain forecasts and forward-looking information about possible or assumed future performance, exploration results, resources or potential growth of Argent Minerals Limited, industry growth or other trend projections.
Such forecasts and information are not a guarantee of future performance and involve unknown risks and uncertainties, as well as other factors, many of which are beyond the control of Argent Minerals Limited.
Actual results and developments may differ materially from those expressed or implied by these forward-looking statements, depending on a variety of factors.
Nothing in this material should be construed as either an offer to sell or a solicitation of an offer to buy or sell securities.

## Slide 26
Acknowledgement to
Argent Minerals Limited